## Slide 1
Re-Imagine North Watt
Corridor Plan Corridor Advisory Team Meeting #1 April 10, 2024
Josh Pilachowski, PhD, TE, RSP1
Senior Transportation Engineer
josh@dksassociates.com
510.295.9741

## Slide 2
Project Background
Project Toolbox
Alternative Review
Next Steps
AGENDA

## Slide 3
Project Background

## Slide 4
North Watt Avenue Corridor Plan (2012)
  Guide infill growth and public improvements
  20-year planning horizon
  Expansion of transit with mixed use development
Designation of the Corridor as a Smart Growth Street
  Requirements for vehicle travel
  Need for continuous bike and pedestrian facilities that meet design standards
Location of the Corridor within an Environmental Justice community (2019)
Updated Corridor Plan funded by Caltrans Sustainable Communities Grant (2022)
Project Background

## Slide 5
North Watt Avenue
  Antelope Road to Peacekeeper Way
  3.0 Mile Corridor
  4-6 Lanes; 35 mph-45 mph speed limit
Adjacent Land Use
  Variety of commercial use either directly adjacent or part of larger combined facilities
  Churches, schools, and community centers
  Residential uses either directly accessible or on adjacent frontage roads elements
Study Area Extent

## Slide 6
Schedule and Status
Existing Conditions and Site Review
Alternatives Analysis
Existing Conditions Report
Alternative Screening
Alternative Identification
Recommended Final Alternative
Summary Report
Implementation Plan
Draft Report
Final Report
Outreach
Board Presentation
Committee
Presentations
Adoption
Community Workshop
Community Charette
Community Workshop
Focus Groups
Stakeholder Interviews and Surveys
Corridor Advisory Team
Corridor Advisory Team
Corridor Advisory Team
April 20

## Slide 7
The corridor is characterized by:
  Inconsistent sidewalk and bicycle facilities
  Lack of access to key locations and services
  Growing vehicular demand
  High collision rates at key intersections
Goal is to re-imagine North Watt Avenue as a multimodal, sustainable, and safe corridor that meets the needs of all users today and in the future. This project will:
  Provide a comfortable and safer traveling environment for vulnerable road users
  Improve facilities to meet current ADA requirements and County design standards
  Provide transit infrastructure which improves user experience
  Accommodate future traffic growth without excessive traffic congestion
  Improve safety for all road users
Purpose and Need Statement

## Slide 8
Project Toolbox

## Slide 9
Streetscape elements overview
MOBILITY
LANDSCAPE
STREET FURNISHING
PLACEMAKING
SAFETY

## Slide 10
MOBILITY
    Bus-stops/ Shelters
    Micro-mobility
    Protected Bike Lanes

## Slide 11
SAFETY
    Bulb-outs
    Pedestrian Beacons
    Enhanced Crosswalks

## Slide 12
LANDSCAPE
    Street Planting & Landscape Strips
    Rain Gardens

## Slide 13
STREET FURNISHING
    Seating/ Benches
    Lighting
    Trash Receptacles
    Signage/ Wayfinding

## Slide 14
PLACEMAKING
    Identity Signage
    Public Art
    Gateway Element

## Slide 15
Roadway Elements Overview
Transit
Vehicle
Bicycle

## Slide 16
Transit Facilities
Images Source: Transit Street Design Guide, NACTO, Accessed April 9, 2024
Bus Queue Jumps
Island Stops

## Slide 17
Urban Boulevard
Roadway Facilities
Image Source: Esplanade Corridor Safety and Accessibility Study, Chico, CA; W-Trans, September 9, 2016
Image Source: Google Earth Street View, Esplanade, Chico, CA
Image Source: Google Earth Street View, Esplanade, Chico, CA

## Slide 18
Urban Boulevard
Roadway Facilities
Image Source: Urban Street Design Guide, NACTO, Accessed April 9, 2024
Image Source: Google Earth Street View, Octavia Street, San Francisco, CA
Image Source: Urban Street Design Guide, NACTO, Accessed April 9, 2024; Original Photo credit to Urbanlandscapes.info

## Slide 19
Class I Bike Trail
Bicycle Facilities
Images Source: DIB 94 Complete Streets: Contextual Design Guidance, Caltrans, January 16, 2024

## Slide 20
Bicycle Facilities
Class IV Bike Lanes
Images Source: DIB 89-02 Class IV Bikeway Guidance, Caltrans, February 7, 2022

## Slide 21
Alternatives

## Slide 22
Project Alternative Concepts
Minimum Improvements
Bring corridor up to current design standards
Sidewalk and bike lane gap closures
One-Way Couplet
Conceives North Watt Avenue as one way northbound and 34th Steet as one way southbound
Study from 2012 had this cross section as three travel lanes, one BRT lane, and one class II bike lane
Current recommendation for this alternative based on feedback removes the BRT lane and replaces the Class II bike lanes with a Class I Trail on North Watt Avenue
Vehicle/Bicyclist Priority Improvement
Options for either four or six lane cross sections
If a four lane cross section is used, requires improvements to 34th Street
Install Class IV buffered bike lanes along Watt Avenue
Urban Boulevard
Improve and expand the frontage road system along Watt Avenue
Provide lower stress bicycle and pedestrian connections along the frontage roads
Limit conflicting driveways for through traffic on Watt Avenue

## Slide 23
Project Alternative Concepts
Cross Sections Generated with Open StreetMix
Cross Sections illustrative, actual dimensions for design will vary by location along the corridor
Minimum Build
One-Way Couplet
Vehicle/Bicyclist Priority Improvement
Urban Boulevard
34th Street
Watt Avenue

## Slide 24
Minimum Improvements
B
C
D
Outcomes
Low Cost and Low Right of Way (ROW) Impact
Brings the corridor in line with current engineering standards with minimal impact to existing homes and businesses
Would not meet the needs of future traffic growth anticipated along Watt Avenue
Corridor would still be high stress for pedestrians and Bicyclists
Key Aspects of Improvement
Bring the existing sidewalks and bicycle lanes up to standard
Close the existing gaps in pedestrian and bicycle infrastructure
Provide frontage improvements where feasible
Cross Sections Generated with Open StreetMix
Cross Sections illustrative, actual dimensions for design will vary by location along the corridor

## Slide 25
One Way Couplet
A
C
D
Outcomes
High cost of improvement and requires significant ROW acquisition on 34th Street
Additional ROW and design challenges for transition points
Brings the corridor in line with current engineering standards
Provides sufficient through capacity for commuters
Requires significant improvement on multiple cross streets between Watt Avenue and 34th street
Would provide potential for significant improvement to bicycle access
Significantly increases walking distance for access to/from southbound transit
Key Aspects of Improvement
Narrows the existing Watt Avenue to three lanes Northbound and improves 34th Street to three lanes southbound
Provides a Class I Bike trail or Bus Rapid Transit (BRT) lanes in the corridor
Cross Sections Generated with Open StreetMix
Cross Sections illustrative, actual dimensions for design will vary by location along the corridor
34th Street
Watt Avenue

## Slide 26
Vehicle/Bicycle Priority
B
D
Outcomes
Middle cost improvement with additional ROW only needed in portions of the corridor
Brings the corridor in line with current engineering standards
Provides sufficient through capacity for growth
Does not impact 34th Street
Would provide significant improvement to bicycle access
Key Aspects of Improvement
Widens the existing Watt Avenue to accommodate six lanes of traffic for most of the study corridor
Adds Class IV buffered bike lanes to both sides of the street
Improves sidewalk and frontage to improve pedestrian comfort
Cross Sections Generated with Open StreetMix
Cross Sections illustrative, actual dimensions for design will vary by location along the corridor

## Slide 27
Urban Boulevard
C
Outcomes
Highest cost improvement with additional ROW needed throughout the corridor
Brings the corridor in line with current engineering standards
Provides sufficient through capacity for growth
Does not impact 34th Street
Would provide significant improvement for pedestrians and bicyclists
Key Aspects of Improvement
Widens the existing Watt Avenue to accommodate six lanes of traffic for most of the study corridor
Adds one way frontage roads to much of the corridor and converts existing two-way frontage to one way
Places a significant buffer between the main travel lanes and the frontage streets which prioritize pedestrian and bicycle activity
Reduces vehicle conflicts for through lanes on Watt Avenue
Cross Sections Generated with Open StreetMix
Cross Sections illustrative, actual dimensions for design will vary by location along the corridor

## Slide 28
Next Steps

## Slide 29
Alternative Refinement
  Public Workshop #2 – April 20, 2024
  Detailed alternative description
Evaluation and Selection of Preferred Alternative
  Comparative review of each alternative
  Cost estimation and displacement analysis
Outreach
  Raising awareness of the preferred alternative
Next Steps

## Slide 30
THANK YOU
Josh Pilachowski, PhD, TE, RSP1
Senior Transportation Engineer
josh@dksassociates.com
510.295.9741